## Slide 1
AI-Based FDM 3D Printing Defect Detection
CNN transfer learning system for automated print quality inspection
96.52%
Test Accuracy
8
Detected Classes
4405
Images
96.50%
Weighted F1
Application Purpose
- Automatically classify FDM 3D printing defects from camera images
- Provide confidence score, likely causes, and corrective actions
1

## Slide 2
Problem Statement
Manual inspection limitations
- Slow and inconsistent
- Defects may appear while print is still running
- Failed prints waste time, filament, and machine usage
AI solution
- Camera image is passed to a CNN
- Model predicts defect category
- System gives feedback for quality control
2

## Slide 3
Dataset
Expanded dataset
- Merged Kaggle FDM defect datasets
- Folder-per-class image classification format
- 0 corrupt images found
- Classes: Cracking, Layer_shifting, No_defect, Off_platform, Spaghetti, Stringing, Under_extrusion, Warping
3083
Training
661
Validation
661
Testing
224x224
Input Size
3

## Slide 4
Defects Detected
Detected classes
- Cracking
- Layer_shifting
- No_defect
- Off_platform
Detected classes
- Spaghetti
- Stringing
- Under_extrusion
- Warping
4

## Slide 5
Model Architecture
EfficientNetB0 transfer learning
Pipeline
- Input image resized to 224 x 224
- Data augmentation improves robustness
- EfficientNetB0 backbone extracts visual features
- Dense softmax layer predicts 8 classes
- Class weighting handles imbalanced classes
- Fine-tuning adapts ImageNet features to FDM defects
5

## Slide 6
Training Workflow
Workflow
- Load and inspect dataset
- Stratified train/validation/test split
- Train classifier head
- Fine-tune final EfficientNet layers
- Save best validation model
- Evaluate on held-out test set
- Generate confusion matrix and classification report
6

## Slide 7
Final Results
96.52%
Test Accuracy
96.95%
Macro F1
96.50%
Weighted F1
0.1058
Test Loss
Key observation
- Most defect classes achieved high F1-score
- No_defect and Under_extrusion are comparatively harder due to visual similarity
- Result is strong for mixed datasets and real-world image variation
7

## Slide 8
Training Curves
Training and validation accuracy/loss across training phases
8

## Slide 9
Confusion Matrix
Class-wise correct and incorrect predictions on the test set
9

## Slide 10
Per-Class Performance
precision recall f1-score support Cracking 0.9855 0.9577 0.9714 71 Layer_shifting 0.9815 0.9815 0.9815 54 No_defect 0.9837 0.8963 0.9380 135 Off_platform 0.9333 1.0000 0.9655 14 Spaghetti 0.9730 1.0000 0.9863 36 Stringing 0.9783 1.0000 0.9890 135 Under_extrusion 0.9161 0.9704 0.9424 135 Warping 0.9756 0.9877 0.9816 81 accuracy 0.9652 661 macro avg 0.9659 0.9742 0.9695 661 weighted avg 0.9662 0.9652 0.9650 661
10

## Slide 11
Interactive Demo
App features
- Continuous OpenCV camera scanning
- Five-prediction temporal averaging
- Uncertainty warning below 60%
- AI feedback and risk level
- Axis and nozzle inspection guidance
- Optional OctoPrint telemetry
Recommended launch
cd /home/ron/ml/fdm_defect_detection
.venv/bin/python src/live_dashboard.py
Open:
http://127.0.0.1:8765
Camera releases when page closes
11

## Slide 12
AI Feedback and Telemetry
Beyond classification
- Predicts class, confidence, and operational risk
- Maps defects to likely causes and corrective actions
- Marks low-confidence frames as uncertain
- Shows temperature and progress when OctoPrint is connected
- Keeps unavailable values explicit instead of fabricating telemetry
- Never moves axes or changes heaters automatically
12

## Slide 13
Limitations
Current limitations
- Model predicts image-level class, not bounding-box location
- 96.52% is an image-level held-out result
- Cross-printer and cross-recording generalization is not yet established
- Accuracy may change with camera angle, lighting, printer, or material
- Monitoring is decision support, not closed-loop control
13

## Slide 14
Future Work
Possible improvements
- Add more classes: over-extrusion, nozzle clog, blobs/zits, layer separation
- Add YOLO-based defect localization
- Use Grad-CAM in live feedback
- Collect own printer-camera dataset
- Add human-approved closed-loop correction
14

## Slide 15
Conclusion
Conclusion
- Built an eight-class AI system for FDM defect detection
- EfficientNetB0 achieved 96.52% image-level test accuracy
- OpenCV dashboard provides continuous monitoring and uncertainty handling
- Explainability, feedback, and optional telemetry support operator decisions
- External printer-session validation remains the next research step
15